## Slide 1: Breaking SIMD Shackles with an Exposed Flexible Microarchitecture and the Access Execute PDG
Venkatraman Govindaraju, Tony Nowatzki, Karthikeyan Sankaralingam
University of Wisconsin-Madison

## Slide 2: Motivation
SIMD (Single Instruction Multiple Data)
  Exploits data level parallelism
  Great for performance and energy
  Examples: X86’s SSE/AVX, ARM’s NEON
Programming for SIMD
  Assembly or compiler intrinsics
  Preferred: Auto-vectorization
Compilers fail to auto-vectorize on most cases*
How can we broaden the scope of vectorization?
* S. Maleki et al. An evaluation of vectorizing compilers. In PACT 2011

## Slide 3: An Example
//Needleman Wunsch
int a[],b[]; //initialize
for(int i =1; i < NCOLS; ++i) {
for(int j = 1; j < NROWS; ++j) {
a[i][j]=max(a[i-1][j-1]+b[i][j],
a[i-1][j],
a[i][j-1]);
}
}
Outer Iterations are
dependent, too
Use result of
previous iteration
Dependence Chain
Array a[][]
Compilers do not map this code to SIMD unit

## Slide 4: SIMD Shackles: Its Interface to Compiler
Memory/Vector Register File
Fixed mem. interface
Fixed parallel datapath
No control flow

## Slide 5: Our Solution Flexible Microarchitecture (DySER)
Memory/Vector Register File
Flexible mem. interface
Configurable datapath
Control flow support

## Slide 6: Our Solution Flexible Microarchitecture (DySER)
Memory/Vector Register File
Flexible Mem. Interface
Configurable datapath
Control flow support
Expose a flexible microarchitecture to compiler
Capture the complexity with AEPDG, a variant of PDG
Design and Implement a compiler with AEPDG

## Slide 7: Executive Summary
Identify microarchitecture techniques required to tackle the challenges with vectorization
Develop AEPDG, a variant of program dependence graph to model the flexible microarchitecture.
Design and implement compiler optimizations with AEDPG.
Demonstrate how our solution broadens the scope of SIMD
Evaluate on throughput benchmarks and show that our solution outperforms ICC on SSE/AVX by 1.8x.

## Slide 8: Outline
Introduction
Flexible Architecture: DySER
Access Execute PDG (AEPDG)
Compiler Design and Optimizations
Evaluation
Conclusion

## Slide 9: DySER Overview
DySER
Circuit-switched array of functional units
Integrated to processor pipeline
Dynamically creates specialized datapath
Fetch Decode Execute Memory WriteBack
D$
I$
Register
File
Decode
Exec
Units
[HPCA 2011]

## Slide 10: Flexible Microarchitecture: Configurable Datapath
Configure switches and functional units to create different datapath
Can specialize datapath
  For ILP
  For DLP
Allows the compiler to use DySER to accelerate variety of computation patterns
×
S
S
S
S
S
S
S
S
×
S
+
S
×
S
+
S
S
S
S
+
S
Mul-Accumulate
-
S
S
S
S
S
S
&
S
S
S
>
S
S
S
S
S
?:
S
+
S
Sum of Abs. Differences
×
S
S
S
S
S
S
+
S
S
×
S
+
S
×
S
+
S
S
S
S
S
3x3 Convolution

## Slide 11: Flexible Microarchitecture: Control Flow Mapping
S
S
S
S
S
S
S
S
>
S
+
S
S
-
S
S
S
S
φ
S
Predication
  Predicates the output
  A metabit in datapath propagates the validity of the data
“Select” function unit (PHI functions)
  Selects valid input and forwards as its output
in0
in1
Out
Pred.
V
V
PHI
V
0
1
1
in1
Native control flow mapping allows compilers to use DySER to accelerate code with arbitrary control-flow

## Slide 12: Flexible Microarchitecture: Decoupled Access/Execute Model
Memory access instructions execute in processor pipeline
  Address Calculation, Loads, and Stores
  Configure DySER
  Send Data to DySER
  Recv Data from DySER
Computation executes in DySER
Processor
DySER
Config
____________
____________
____________
x
-
+
+
+
x
-
+
+
+
____________
____________

## Slide 13: Flexible Microarchitecture: Decoupled Access/Execute Model
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
Input
FIFO
Output
FIFO
IP0
IP1
IP2
IP3
OP0
OP1
OP2
OP3
Processor sends data to DySER through its input FIFOs (input ports)
DySER computes in data flow fashion
Processor receives data from DySER through its output FIFOs (output ports)
Decoupled Access/Execute model allows DySER to consume data in different order than how it is stored

## Slide 14: Flexible Microarchitecture: Flexible Vector Interface
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
IP0
IP1
IP2
IP3
3
2
1
0
7
6
5
4
Memory/
Vector register
0
1
2
3
0
1
2
3
0
1
2
3
“Vector Port Mapping”
Flexible vector interface allows compiler to use DySER to code with different memory access patterns (eg. Strided)

## Slide 15: Outline
Introduction
Flexible Architecture: DySER
Access Execute PDG
Compiler Design and Optimizations
Evaluation
Conclusion

## Slide 16: Access Execute Program Dependence Graph (AEPDG)
A variant of PDG
Edges represent both data and control dependence
Explicitly partitioned into access-PDG and execute-PDG subgraph
Edges between access and execute-PDG augmented with temporal information
for (i = 0; i < N; ++i)
if b[i] < 0:
a = b[i] + 5;
else:
a = b[i] - 5;
b[i]=a;
-
+
<
LD
ST
φ
b+i
+
-
<
φ

## Slide 17: AEPDG and Flexible Interface
×
×
×
+
+
a[i]
a[i+1]
a[i+2]
out[i]
×
×
×
+
+
a[i]
a[i+1]
a[i+2]
out[i]
a[i+3]
a[i+4]
a[i+5]
out[i+1]
0
3
1
4
2
5
P0
P1
P2
P3
×
×
×
0
1
3
2
4
5
7
6
0
1
0
1
0
1
1
0
Vector Port (for a[])
Original AEPDG
Unrolled AEPDG
Vector Map Generation
(Load/Store Coalescing)
x
x
x
x
x
x
x
x
Vector Port Map
P0
x
P0
x
x
x
x
x
P0
P1
P0
x
P1
x
x
x
P0
P1
P0
P2
P1
P2
x
x
Each edge on the interface knows its order

## Slide 18: AEPDG and Flexible Interface
×
×
×
+
+
a[i]
a[i+1]
a[i+2]
out[i]
×
×
×
+
+
out[i]
out[i+1]
0
4
1
5
2
6
P0
P1
P2
P3
×
×
×
0
1
3
2
4
5
7
6
1
0
Vector Port (for a[])
Original AEPDG
Unrolled AEPDG
Vector Map Generation
x
x
x
x
x
x
x
x
Vector Port Map
P0
x
x
x
P0
x
x
x
P0
P1
x
x
P0
P1
x
x
P0
P1
P0
P2
P1
P2
x
x
a[i:i+5]
Each edge on the interface knows its order

## Slide 19: Outline
Introduction
Flexible Architecture: DySER
Access Execute PDG
Compiler Design and Optimizations
Evaluation
Conclusion

## Slide 20: Compilation Tasks
Identify loops to specialize
Construct AEPDG
  Access PDG
  Execute PDG
Perform Optimizations
  Vectorization, if possible
Schedule
  Execute PDG to DySER
  Access PDG to Core
Core aaa
DySER
Scheduling
Optimization
Execute Code
Access Code
Region Identification Partitioning
Application

## Slide 21: Small loops
We can again leverage loop properties.
  Simply unroll the loop further, “Cloning” the region
×
+
a[0]
a[1]
a[2]
a[3]
b[0]
b[1]
b[2]
b[3]
c[0]
c[1]
c[2]
c[3]
×
+
a[0]
a[2]
b[0]
b[2]
c[2]
c[0]
×
+
a[1]
a[3]
b[1]
b[3]
c[3]
c[1]
Input
FIFO
Output
FIFO
Execute
Region
Before
After
Also Uses
Flexible I/O

## Slide 22: Large Loops: Sub-graph Matching
Subgraph Matching
  Find Identical computations, split them out
Region Splitting
  Configure multiple regions, quickly switch between them
Large Region
Subgraph Matching
Region Virtualization

## Slide 23: Loop Dependence
//Needleman Wunsch
int a[],b[]; //initialize
for(int i =1; i < NCOLS; ++i) {
for(int j = 1; j < NROWS; ++j) {
a[i][j]=max(a[i-1][j-1]+b[i][j],
a[i-1][j],
a[i][j-1])
}
}
Outer Iterations are
dependent, too
+
max
max
a[i-1][j-1]
a[i-1][j]
Use result of
previous iteration
a[i][j-1]
a[i][j]
+
max
max
a[i-1][j]
a[i-1][j+1]
a[i][j+1]
Vectorizable!
Dependence Chain
Array a[]
+
max
max
+
max
max

## Slide 24: Outline
Introduction
Flexible Architecture: DySER
Access Execute PDG
Compiler Design and Optimizations
Evaluation
Conclusion

## Slide 25: Evaluation Methodology
Implementation
  Leverages LLVM compilation framework
  Constructs AEPDG from LLVM-IR
  Generates binary for x86, SPARC
Benchmarks
  Throughput kernels
  Parboil benchmarks
Simulation framework
  Gem5 + DySER
  Evaluated DySER with a 4-wide out-of-order core
  Compared ICC auto-vectorizer to DySER compiler

## Slide 26: SSE/AVX Vs. DySER
Chart: Speedup Over SSE
| CONV | MERGE | NBODY | RADAR | TREESEARCH | VR | CutCP | FFT | KMEANS | LBM | MM | MRI-Q | SPMV | STENCIL | TPACF | NNW | NEEDLE | HM
SSE | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
AVX | 1.6286 | 1 | 1.8611 | 1.7368 | 1 | 1 | 1 | 1 | 1 | 1 | 1.1429 | 2.25 | 1 | 1.0435 | 1 | 1 | 1 | 1.133
DySER | 2.6657 | 3.06 | 1.3333 | 4.9711 | 2.24 | 0.99 | 1.2964 | 1.26 | 1.2632 | 1.42 | 3.4071 | 3.705 | 1.27 | 1.4928 | 13.36 | 1 | 2.37 | 1.7547
13x
DySER bottlenecked by FDIV/FSQRT units
DySER performs on average 1.8x better than SSE/AVX
When DLP readily available, both SIMD and DySER perform better
With control intensive code, DySER perform better

## Slide 27: Programmer Optimized vs. Compiler Optimized
Chart: Relative to programmer optimized
| CONV | MERGE | NBODY | RADAR | TREESEARCH | VR | CutCP | FFT | KMEANS | LBM | MM | MRI-Q | SPMV | STENCIL | TPACF | NNW | NEEDLE | HM
Compiler | 0.91921 | 0.91071 | 0.82474 | 0.8213 | 1 | 0.67114 | 0.67598 | 0.38415 | 0.76656 | 0.80682 | 0.59625 | 1 | 0.7341 | 0.95963 | 1.0245 | 0.50163 | 0.58809 | 0.7239
Outer Loop Transformations
Different strategy for Reduction
Constant Table Lookup
Compiler generated code’s slowdown is only 30%

## Slide 28: Conclusion
Broke the “SIMD Shackles” with flexible microarchitecture
Managed the complexity of the microarchitecture interface with AEPDG
Compilers build using AEPDG can broaden the scope of SIMD
Must rethink accelerators and their interface to compiler
  Incremental changes to accelerators leads to diminishing returns

## Slide 29: Questions?
DySER compiler available at
http://research.cs.wisc.edu/vertical/dyser-compiler