## Slide 1: Memory-centric System Interconnect Design with Hybrid Memory Cubes
Gwangsun Kim, John Kim
Korea Advanced Institute of Science and Technology
Jung Ho Ahn, Jaeha Kim
Seoul National University

## Slide 2: Memory Wall
Core count – Moore’s law : 2x in 18 months.
Pin count – ITRS Roadmap : 10% per year.
 core growth >> Memory bandwidth growth
Memory bandwidth can continue to become bottleneck
Capacity, energy issues and so on..
[Lim et al., ISCA’09]

## Slide 3: Hybrid Memory Cubes (HMCs)
Solution for memory bandwidth & energy challenges.
HMC provides routing capability  HMC is a router
DRAM layers
Logic layer
Processor
High-speed signaling
TSV
MC
MC
MC
…
I/O
I/O
I/O
Interconnect
…
Ref.: “Hybrid Memory Cube Specification 1.0,” [Online]. Available: http://www.hybridmemorycube.org/,
Hybrid Memory Cube Consortium, 2013.
How to interconnect multiple CPUs and HMCs?
(Packetized high-level messages)
Packet

## Slide 4
Memory
Network
…
HMC
HMC
HMC
…
HMC
HMC
HMC
HMC
Memory Network
CPU
CPU

## Slide 5: Interconnection Networks
On-chip
Interconnection networks
Supercomputers
Cray X1
Router
fabrics
Avici TSR
I/O
systems
Myrinet/Infiniband
MIT RAW
Memory

## Slide 6: How Is It Different?
 | Interconnection Networks (large-scale networks) | Memory Network
Nodes vs. Routers
Network
Organization
Important Bandwidth
Cost
Others
# Nodes ≥ # Routers
# Nodes < # Routers (or HMCs)
Concentration
Distribution
Bisection Bandwidth
CPU Bandwidth
Channel
Channel
Intra-HMC network
“Routers” generate traffic

## Slide 7: Conventional System Interconnect
Intel QuickPath Interconnect / AMD HyperTransport
Different interface to memory and other processors.
CPU1
CPU3
CPU0
CPU2
Shared parallel bus
High-speed P2P links

## Slide 8: Adopting Conventional Design Approach
CPU can use the same interface for both memory/other CPUs.
CPU bandwidth is statically partitioned.
CPU1
CPU3
CPU0
CPU2
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
HMC
Same links

## Slide 9: Bandwidth Usage Ratio Can Vary
Ratio of QPI and Local DRAM traffic for SPLASH-2.
    Real quad-socket Intel Xeon system measurement.
We propose Memory-centric Network to achieve flexible CPU bandwidth utilization.
Chart: Local DRAM /QPI bandwidth usage ratio
| Radiosity | Raytrace | FMM | Cholesky | Barnes | LU | Radix | FFT | Ocean
Local DRAM BW/QPI BW ratio | 0.8 | 0.84375 | 0.94828 | 1.1486 | 1.263 | 1.3976 | 1.7288 | 1.7377 | 1.8356
~2x difference in coherence/memory traffic ratio

## Slide 10: Contents
Background/Motivation
Design space exploration
Challenges and solutions
Evaluation
Conclusions

## Slide 11: Leveraging Routing Capability of the HMC
Local HMC traffic BW
CPU-to-CPU traffic BW
CPU
CPU
HMC
Conventional Design
Memory-centric Design
50%
50%
100%
100%
Bandwidth Comparison
HMC
HMC
HMC
HMC
HMC
HMC
HMC
CPU bandwidth can be flexibly utilized for different traffic patterns.
Other CPUs
Other HMCs
Coherence
Packet

## Slide 12: System Interconnect Design Space
…
CPU
…
CPU
Network
…
Processor-centric
Network (PCN)
HMC
HMC
HMC
HMC
CPU
…
…
Network
…
CPU
Memory-centric
Network (MCN)
HMC
HMC
HMC
HMC
…
CPU
…
CPU
Network
…
Network
Hybrid Network
HMC
HMC
HMC
HMC

## Slide 13: Interconnection Networks 101
Average packet latency
Offered load
Latency
  Distributor-based Network
  Pass-thru Microarchitecture
Throughput
  Distributor-based Network
  Adaptive (and non-minimal routing)
Zero-load latency
Saturation throughput

## Slide 14: Memory-centric Network Design Issues
Key observation:
    # Routers ≥ # CPUs
Large network diameter.
CPU bandwidth is not fully utilized.
Mesh
CPU
CPU
CPU
CPU
CPU
CPU
Flattened Butterfly [ISCA’07]
CPU
CPU
CPU
CPU
Dragonfly [ISCA’08]
5 hops
CPU
CPU
group

## Slide 15: Network Design Techniques
Network
CPU
…
CPU
…
Baseline
CPU
HMC
HMC
HMC
CPU
CPU
…
Concentration
CPU
CPU
…
Network
…
HMC
HMC
Network
CPU
…
Distribution
…
CPU
…
HMC
HMC
HMC
HMC

## Slide 16: Distributor-based Network
Distributor-based Dragonfly
Distribute CPU channels to multiple HMCs.
  Better utilize CPU channel bandwidth.
  Reduce network diameter.
Problem: Per hop latency can be high
  Latency = SerDes latency + intra-HMC network latency
3 hops
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
Dragonfly [ISCA’08]
5 hops

## Slide 17: Reducing Latency: Pass-thru Microarchitecture
Reduce per-hop latency for CPU-to-CPU packets.
Place two I/O ports nearby and provide pass-thru path.
  Without serialization/deserialization.
5GHz Rx Clk
DES
RC_A
SER
RC_B
5GHz Tx Clk
Input port A
Output port B
Datapath
Datapath
Fall-thru path
Pass-thru path
DRAM (stacked)
Memory Controller
Channel
I/O port
Pass-thru

## Slide 18: Leveraging Adaptive Routing
Memory network provides non-minimal paths.
Hotspot can occur among HMCs.
  Adaptive routing can improve throughput.
Minimal path
H0
H1
H2
H3
CPU
…
…
…
…
Non-minimal path

## Slide 19: Methodology
Workload
  Synthetic traffic: request-reply pattern
  Real workload: SPLASH-2
Performance
  Cycle-accurate Pin-based simulator
Energy:
  McPAT (CPU) + CACTI-3DD (DRAM) + Network energy
Configuration:
  4CPU-64HMC system
  CPU: 64 Out-of-Order cores
  HMC: 4 GB, 8 layers x 16 vaults

## Slide 20: Evaluated Configurations
Configuration Name | Description
PCN | PCN with minimal routing
PCN+passthru | PCN with minimal routing and pass-thru enabled
Hybrid | Hybrid network with minimal routing
Hybrid+adaptive | Hybrid network with adaptive routing
MCN | MCN with minimal routing
MCN+passthru | MCN with minimal routing and pass-thru enabled
Representative configurations for this talk.
More thorough evaluation can be found in the paper.

## Slide 21: Synthetic Traffic Result (CPU-Local HMC)
Each CPU sends requests to its directly connected HMCs.
MCN provides significantly higher throughput.
Latency advantage depends on traffic load.
Chart: Offered load (GB/s/CPU)
| 5.76 | 8.64 | 11.52 | 20.16 | 28.8 | 37.44 | 46.08 | 54.72 | 63.36 | 72.0 | 80.64 | 89.28 | 97.92 | 106.56 | 115.2 | 123.84 | 132.48 | 141.12 | 149.76 | 158.4 | 167.04 | 175.68 | 184.32 | 192.96 | 201.6 | 210.24 | 218.88 | 227.52
PCN | 60.1696 | 60.3517 | 60.4676 | 61.1638 | 61.8035 | 62.7501 | 63.8795 | 65.4802 | 67.4861 | 71.4728 | 77.8053 | 93.0664 | 208.3336 | 665.728 | 1203.44 | 1678.168 | 2124.704 | 2523.208 | 2845.816 | 3146.648 | 3428.752 | 3689.528 | 3867.48 | 4089.984 | 4268.736 | 4429.416 | 4585.376 | 4743.448
PCN+passthru | 48.4971 | 48.8049 | 49.0636 | 50.1987 | 51.0251 | 52.4317 | 53.9897 | 55.8663 | 58.0524 | 61.8026 | 67.974 | 83.2152 | 269.7672 | 767.7424 | 1278.624 | 1782.312 | 2167.336 | 2539.384 | 2880.616 | 3179.392 | 3395.416 | 3625.752 | 3856.464 | 3978.424 | 4154.536 | 4365.008 | 4475.856 | 4567.776
Hybrid | 56.5021 | 56.6506 | 57.2286 | 57.4143 | 58.0877 | 58.9847 | 60.1654 | 62.1213 | 64.2346 | 68.5582 | 76.8593 | 90.8584 | 224.7616 | 694.888 | 1246.904 | 1729.584 | 2153.568 | 2549.536 | 2847.48 | 3147.16 | 3458.72 | 3674.136 | 3899.736 | 4090.36 | 4302.192 | 4481.8 | 4600.488 | 4754.632
MCN | 54.5599 | 54.7383 | 54.6611 | 55.0872 | 55.4606 | 55.689 | 56.2833 | 56.7802 | 57.6119 | 58.2409 | 59.1434 | 60.2658 | 61.4527 | 63.2996 | 65.4776 | 68.4561 | 72.5344 | 79.2364 | 90.5456 | 116.0592 | 229 | 506.5064 | 805.488 | 1151.448 | 1402.008 | 1732.168 | 1961.84 | 2207.864
Average transaction latency (ns)
50% higher throughput
PCN+passthru is better
MCN is better

## Slide 22: Synthetic Traffic Result (CPU-to-CPU)
CPUs send request to other CPUs.
Using pass-thru reduced latency for MCN.
Throughput: PCN < MCN+pass-thru < Hybrid+adaptive routing
Chart: Offered Load (GB/s/CPU)
| 5.76 | 5.76 | 8.64 | 11.52 | 14.4 | 17.28 | 20.16 | 23.04 | 25.92 | 28.8 | 31.68 | 34.56 | 37.44 | 40.32 | 43.2 | 46.08 | 48.96 | 51.84 | 54.72 | 57.6 | 60.48 | 63.36 | 66.24 | 69.12 | 72.0 | 74.88 | 77.76 | 80.64 | 83.52 | 86.4 | 89.28 | 92.16 | 95.04 | 97.92 | 100.8 | 103.68 | 106.56 | 109.44 | 112.32
PCN | 53.8198 | 53.8198 | 54.202 | 55.06 | 55.7554 | 56.8753 | 58.1499 | 60.3612 | 63.3803 | 68.4076 | 77.5458 | 99.3552 | 219.1928 | 724 | 1179.608 | 1618.552 | 1985.84 | 2370.232 | 2671.168 | 2988.056 | 3156.04 | 3411.568 | 3639.72 | 3814.728 | 4062.36 | 4171.976 | 4362.136 | 4494.408 | 4636.68 | 4752.952 | 4836.016 | 4994.72 | 5066.048 | 5175.384 | 5287.304 | 5339.552 | 5415.448 | 5513.376 | 5621.312
Hybrid | 53.6797 | 53.6797 | 54.3005 | 55.0398 | 55.7069 | 57.0364 | 58.5046 | 60.6073 | 63.401 | 69.0334 | 80.8568 | 108.7776 | 210.3432 | 721.6568 | 1196.816 | 1702.432 | 1930.856 | 2350.32 | 2646.832 | 2878.664 | 3173.32 | 3313.528 | 3623.616 | 3785.504 | 3949.92 | 4065.456 | 4298.712 | 4275.256 | 4651.928 | 4704.448 | 4836.512 | 4877.008 | 4943.992 | 5174.912 | 5145.768 | 5278.472 | 5372.896 | 5486.424 | 5540.168
Hybrid+adaptive | 54.0333 | 54.0333 | 54.8941 | 56.0887 | 57.1124 | 58.2186 | 59.1899 | 60.446 | 61.4895 | 62.5605 | 63.6314 | 64.8494 | 66.0255 | 67.3209 | 68.9688 | 70.4466 | 72.2258 | 73.9105 | 76.7235 | 79.9426 | 82.668 | 87.3 | 95.7744 | 117.9288 | 141.428 | 291.5152 | 522.4016 | 792.6144 | 1097.352 | 1244.768 | 1481.496 | 1668.248 | 1821.008 | 2051.416 | 2225.024 | 2375.68 | 2424.096 | 2625.816 | 2690.528
MCN | 76.5935 | 76.5935 | 76.9335 | 77.4044 | 77.7936 | 78.3488 | 79.0472 | 79.8062 | 80.8176 | 81.6936 | 83.2392 | 84.504 | 86.4568 | 88.9256 | 91.9104 | 95.1072 | 101.2336 | 110.96 | 119.7016 | 136.7456 | 173.0368 | 279.052 | 516.9064 | 851.112 | 1081.08 | 1264.584 | 1587.608 | 1737.6 | 2016.912 | 2236.536 | 2374.744 | 2503.888 | 2690.816 | 2918.416 | 3107.272 | 3194.264 | 3172.816 | 3411.96 | 3535.68
MCN+passthru | 60.9559 | 60.9559 | 61.3064 | 61.7318 | 62.144 | 62.4829 | 63.0231 | 63.634 | 64.127 | 64.9731 | 65.9014 | 67.027 | 68.4151 | 69.993 | 71.816 | 74.8866 | 79.8311 | 84.6696 | 90.3312 | 110.7088 | 130.9424 | 314.4008 | 608.9536 | 763.1904 | 1046.736 | 1171.224 | 1402.104 | 1600.904 | 1861.328 | 1953.104 | 2185.048 | 2371.984 | 2432.696 | 2581.944 | 2656.776 | 2831.144 | 2913.944 | 3071.408 | 3139.512
27% Latency reduction by pass-thru
Average transaction latency (ns)
20%
62%
PCN, hybrid is better
MCN is better

## Slide 23: Real Workload Result – Performance
Impact of memory-centric network:
  Latency-sensitive workloads performance is degraded.
  Bandwidth-intensive workloads performance is improved.
Hybrid network+adaptive provided comparable performance.
Chart: 
| Barnes | Cholesky | FFT | FMM | LU | Ocean | Radix | Raytrace | Water-sp | GMEAN
PCN | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PCN+passthru | 0.9799 | 1.0129 | 0.9676 | 0.9117 | 0.9526 | 0.9772 | 0.9696 | 0.9485 | 0.9857 | 0.9629
Hybrid+adaptive | 0.948 | 0.9412 | 0.7826 | 0.9601 | 0.9495 | 0.9806 | 0.8606 | 0.7748 | 0.9789 | 0.8938
MCN+passthru | 0.986 | 0.9077 | 0.7884 | 0.9472 | 0.9293 | 1.0735 | 0.7761 | 0.666 | 1.0008 | 0.8754
33%
12%
Normalized Runtime
7%
22%
23%

## Slide 24: Real Workload Result – Energy
MCN have more links than PCN  increased power
More reduction in runtime  energy reduction (5.3%)
MCN+passthru used 12% less energy than Hybrid+adaptive.
Chart: 
| Barnes | Cholesky | FFT | FMM | LU | Ocean | Radix | Raytrace | Water-sp | GMEAN
PCN | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PCN+passthru | 0.98548 | 1.012 | 0.98137 | 0.93239 | 0.95599 | 0.98152 | 0.97528 | 0.96929 | 0.99306 | 0.97603
Hybrid+adaptive | 1.1389 | 1.08 | 0.99077 | 1.1578 | 1.0267 | 1.1866 | 1.0621 | 0.96625 | 1.07 | 1.0731
MCN+passthru | 1.0354 | 0.96873 | 0.8963 | 1.0062 | 0.95988 | 1.1055 | 0.86976 | 0.72418 | 1.0179 | 0.94749
Normalized Energy
5.3%
12%

## Slide 25: Conclusions
Hybrid Memory Cubes (HMC) enable new opportunities for a “memory network” in system interconnect.
Distributor-based network proposed to reduce network diameter and efficiently utilize processor bandwidth
To improve network performance:
  Latency : Pass-through uarch to minimize per-hop latency
  Throughput : Exploit adaptive (non-minimal) routing
Intra-HMC network is another network that needs to be properly considered.