## Slide 1: McRouter: Multicast within a Router for High Performance NoCs
Yuan He, Hiroshi Sasaki*,
Shinobu Miwa, Hiroshi Nakamura
The University of Tokyo and *Kyushu University

## Slide 2: Executive Summary
Like other networks, NoCs are latency critical. But through evaluations, we also observed that they can be quite bandwidth plentiful (within the routers)
We propose to have packets multicast within a router (routed to all possible outputs), so that route computation is completely hidden and is only required to acknowledge the ONE correctly routed packet in a multicasting
Results show that
  McRouter incurs more productive use of its internal bandwidth
  It outperforms the Prediction Router (the best router so far) with nearly all application traffic we evaluated

## Slide 3: Outline
Scope of the Work
Motivation
Proposal: Multicast within a Router
Evaluations and Results
Conclusion

## Slide 4: Scope
On-chip routers
Standalone router designs
  So not based on look-ahead routing
  Conventional Router
  Prediction Router (HPCA 2009, Matsutani et al)
Mesh topology
  But the idea should be able to other topologies as well

## Slide 5: Motivation
Modern On-chip Networks
  Latency Critical
    NoCs affects cache/memory access latency
  Let us look at two router designs
    Conventional Router (4-cycle)
    Prediction Router (1-cycle when prediction succeeds)

## Slide 6: Conventional Router (CR)
Conventional Virtual Channel Router
  BW/RC -> VA -> SA -> ST
    Problem -> 4 cycles
P
P
P
P
1
2
3
4
BW: Buffer Write
RC: Route Computation
VA: Virtual Channel Allocation
SA: Switch Allocation
ST: Switch Traversal

## Slide 7: Prediction Router (PR, Hit)
Prediction Router (HPCA 2009, Matsutani et al)
  If prediction hits (and VA/SA succeeds with this predicted RC), only ST is needed (1-cycle)
P
P
P
P
1

## Slide 8: Prediction Router (PR, Miss)
Prediction Router
  If prediction misses, miss-routed packets get killed and the conventional data path is then used
  Problem -> prediction accuracy is around 65% in our evaluation
P
P
P
P
1

## Slide 9: Motivation (cont…)
Modern On-chip Networks
  Bandwidth Plentiful
  Observations

## Slide 10: Observation 1: Avearge Link Utilization
Chart: 
| barnes | cholesky | fmm | ocean (cont.) | ocean (non-cont.) | raytrace | volrend | water (nsquared) | water (spatial) | EP | FT | IS | LU
Average Link Utilization | 0.0055856 | 0.016568 | 0.012292 | 0.016937 | 0.028719 | 0.011898 | 0.013582 | 0.0059262 | 0.0048893 | 0.018017 | 0.031375 | 0.02362 | 0.030483
Average Link Utilization (flits/link/cycle)

## Slide 11: Observation 1: Avearge Link Utilization
0.031 flits/link/cycle for the worst case - FT
  0.2 flits / crossbar / cycle assuming a radix-6 router
Little contention internally

## Slide 12: Observation 2: Concurrent Flits to a Router
Chart: 
| barnes | cholesky | fmm | ocean (cont.) | ocean (non-cont.) | raytrace | volrend | water (nsquared) | water (spatial) | EP | FT | IS | LU
0 | 10797166647 | 491604238 | 3796685335 | 1286243002 | 1670634631 | 2533841991 | 1928584924 | 5989028321 | 5600278453 | 2574096833 | 3117278268 | 4276092102 | 1585532677
1 | 354847857 | 46151605 | 267920536 | 129102171 | 277711429 | 180946671 | 150392850 | 203611434 | 162045209 | 271258597 | 557255880 | 599323146 | 290444068
>=2 | 5061106 | 3155511 | 13189065 | 6410839 | 27472630 | 5149762 | 7411073 | 3846893 | 1793726 | 15126061 | 59906690 | 41211697 | 25007750
Fraction of Numbers of Concurrent Flits

## Slide 13: Observation 2: Concurrent Flits to a Router
P
P
Taking the worst case workload – FT
  83% of the time -> no incoming flits
  15% of the time -> 1 flit only
  2 % of the time -> 2+ flits
Very few chances of encountering concurrent flits

## Slide 14: Proposal: Multicast within a Router
Or McRouter for short
  Single-cycle router when having enough bandwidth
  Is based on multicast operation inside a router
  A multicast is like a always-correct prediction
    No predictors
Conventional Router
Prediction Router
McRouter

## Slide 15: McRouter: Conditions to Invoke A Multicasting
Only 1 flit arrives at the router (which means no concurrent flits)
Within this router, no flit is waiting to undertake ST (switch traversal)
P

## Slide 16: Multicasting Operation
P
P
P
P

## Slide 17: A Summary on McRouter
Pros
  A single cycle router when internal bandwidth allows
  No predictors
Cons
  More complex control over the crossbar switch
  Killing of more miss-routed flits

## Slide 18: Evaluation Methodology
CPU Model: Simics 3.0.31
  16 cores, in-order
Memory Model: GEMS 2.1.1
  32KB L1 I/D Caches
  256KB L2 Cache X 16 Banks
  4 Memory Controllers, 4GB main memory
NoC Model: GARNET
  4 X 4 Mesh with virtual channel routers
NoC Power Model: Orion 2
  32nm process and 1V Vdd
Synthetic Traffic: Uniform Radom
Benchmarks: 13 workloads
  From SPLASH-2 and NPB-3
Counterparts: CR and PR
Router
Link
Core/L1$s
L2$
Memory
Controller
Router
Link

## Slide 19: Evaluations with Synthetic Traffic
Chart: Injection Rate (flits/node/cycle)
| 2.5000000000000001E-2 | 0.05 | 7.4999999999999997E-2 | 0.1 | 0.125 | 0.15 | 0.17499999999999999 | 0.2 | 0.22500000000000001 | 0.25 | 0.27500000000000002 | 0.3 | 0.30499999999999999
Conventional Router | 38.8102 | 39.1749 | 39.4152 | 39.7725 | 40.3565 | 40.807 | 41.7973 | 43.0277 | 44.6667 | 47.0883 | 51.4849 | 63.7491 | 69.2086
Prediction Router (LPM) | 35.4894 | 36.1265 | 36.4417 | 37.0708 | 38.0431 | 38.6995 | 39.6433 | 40.7238 | 42.272 | 44.6002 | 48.4547 | 56.8718 | 62.8705
Prediction Router (FCM) | 35.0248 | 35.3666 | 36.0968 | 36.4366 | 37.1838 | 37.8924 | 38.7914 | 40.145 | 41.748 | 43.8152 | 47.5981 | 55.6114 | 59.7396
McRouter | 34.065 | 35.4808 | 36.8776 | 37.8909 | 38.9807 | 40.0202 | 41.3791 | 42.5423 | 44.5988 | 47.1726 | 51.1571 | 62.7582 | 71.2844
0.07 flits/link/cycle
0.34 flits/link/cycle

## Slide 20: Evaluations with Application Traffic: Normalized System Speed-up
Chart: 
| barnes | cholesky | fmm | ocean (cont.) | ocean (non-cont.) | raytrace | volrend | water (nsquared) | water (spatial) | EP | FT | IS | LU | Geometric Mean
Conventional Router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Prediction Router (LPM) | 1.345 | 1.0703 | 1.1985 | 1.1694 | 1.1174 | 1.3164 | 1.2004 | 1.299 | 1.3635 | 1.1639 | 1.1837 | 1.0984 | 1.141 | 1.2017
Prediction Router (FCM) | 1.3861 | 1.0401 | 1.2029 | 1.1727 | 1.144 | 1.337 | 1.2391 | 1.3491 | 1.4018 | 1.1554 | 1.1319 | 1.1098 | 1.1615 | 1.2129
McRouter | 1.4756 | 1.0598 | 1.2659 | 1.2451 | 1.2181 | 1.4482 | 1.3119 | 1.4295 | 1.4812 | 1.2011 | 1.2139 | 1.1326 | 1.2082 | 1.2774

## Slide 21: Sensitivity Study with Network Parameter Downscaling
Chart: Normalized System Speed-up
| 128-bit, 4 VCs | 64-bit, 4 VCs | 128-bit, 1 VC
CR | 1 | 1 | 1
PR(LPM) | 1.3164 | 1.3111 | 1.2958
PR(FCM) | 1.337 | 1.3348 | 1.3074
McRouter | 1.4482 | 1.4242 | 1.4434
Chart: 
| 128-bit, 4VCs | 64-bit, 4 VCs | 128-bit, 1 VC
CR | 1 | 1 | 1
PR(LPM) | 1.1837 | 1.1887 | 1.177
PR(FCM) | 1.1319 | 1.1557 | 1.1514
McRouter | 1.2139 | 1.2434 | 1.2863
Parameters downscaled
  Link width halved
  # of VCs minimized
McRouter still works with thinned bandwidth
  Its advantages over CR/PR is not from over-designing
Workload: raytrace
Workload: FT

## Slide 22: Conclusion
A new low-latency router
  It successfully hides route computation and arbitration delays while still being a standalone design
  It outperforms PR (best router so far) in practice
  We uncover an insight that with more aggressive utilization of remaining internal bandwidth, a router can have its latency dramatically shortened with simple architectural changes

## Slide 23: Thank you so much for attention!